## Slide 1
1
0
1
1
0
0
1
0
1
1
0
1
COMPUTER ORGANIZATION AND ARCHITECTURE
Binary Storage and Registers
How a computer holds a 1, a 0, and a whole number inside the CPU.
Presented by <Your Name>
Roll no. / Section <Roll No>
Theory Presentation · 8 slides
Notes: == SAY THIS (one line) ==
My topic is how a computer stores 1s and 0s, and where it keeps them.
== FULL SCRIPT ==
- Good morning. My topic is Binary Storage and Registers.
- My aim is simple: to answer two questions.
- First, how does a machine that only understands ON and OFF keep a number?
- Second, where does it keep that number while it is calculating?
- By the end you will see that the answer to the first is a tiny circuit called a flip-flop, and the answer to the second is a register.
== IF ASKED ==
Nothing yet - just set up the two questions.

## Slide 2
AGENDA
What we will cover
Six ideas, in the order they build on each other.
01
Binary representation
bits, bases, powers at work: 2ⁿ patterns, KB/MB/GB/TB
02
Storage elements
SR latch, D flip-flop, DRAM capacitor — where one bit lives
03
The register itself
n flip-flops on one clock, plus the CPU's named registers
04
Control and transfer
R1 ← R2, load enable, shift registers, tri-state bus
05
Placement and example
memory hierarchy, then one 8-bit register worked out
06
Summary
five sentences that carry the whole topic
SAY THIS: Six short steps, and each one uses the step before it.
Binary Storage and Registers
02
Notes: == SAY THIS (one line) ==
Six short steps, and each one uses the step before it.
== FULL SCRIPT ==
- Here is the route I will follow, and it is a ladder.
- Step one: bits - what binary is and how many values fit in a few bits.
- Step two: the small circuit that can hold one bit.
- Step three: a register - just many of those circuits in a row.
- Step four: how we control a register, move values between registers, and share one wire between them.
- Step five: where registers sit in the computer, plus one worked example.
- Step six: a short summary, and then your questions.
== IF ASKED ==
No numbers to remember here, just the order.

## Slide 3
01 · REPRESENTATION
Binary: two states, and 2ⁿ patterns
Hardware is cheapest when it only has to tell two states apart — and n bits then give exactly 2ⁿ values.
One byte = 8 bits = 2 hex digits
1
0
1
1
0
1
0
0
b7
b6
b5
b4
b3
b2
b1
b0
MSB ← position weights → LSB
WEIGHTS 128 · 64 · 32 · 16 · 8 · 4 · 2 · 1
128 + 32 + 16 + 4 = 180 1011 0100 → 0xB4
A 0 or 1 is a voltage range, not an exact level, so small electrical noise cannot change it.
Base | Name | Digits | 10110100₂ is
2 | Binary | 0, 1 | 10110100
8 | Octal | 0 – 7 | 264
10 | Decimal | 0 – 9 | 180
16 | Hex | 0 – 9, A – F | 0xB4
How many values fit in n bits?
n | Patterns | Unsigned range | Typical use
1 | 2 | 0 – 1 | flag
8 | 256 | 0 – 255 | byte / ASCII
16 | 65,536 | 0 – 65,535 | half-word
32 | 4.29 × 10⁹ | 0 – 2³²−1 | word / IPv4
64 | 1.84 × 10¹⁹ | 0 – 2⁶⁴−1 | long / address
Storage units are powers of two
1 KB
2¹⁰
1,024 B
1 MB
2²⁰
1,048,576 B
1 GB
2³⁰
1.07 × 10⁹ B
1 TB
2⁴⁰
1.10 × 10¹² B
Why 1024 and not 1000? k address bits select 2ᵏ locations, so capacity lands on powers of two.
SAY THIS: A bit is just ON or OFF. Each extra bit doubles the values you can store.
Binary Storage and Registers
03
Notes: == SAY THIS (one line) ==
A bit is just ON or OFF. Each extra bit doubles the values you can store.
== FULL SCRIPT ==
- Everything inside a computer is either ON or OFF. We write ON as 1 and OFF as 0, and one such digit is called a bit.
- Why only two states? Because a transistor that is fully off or fully on is cheap, fast, and does not get confused by small electrical noise.
- Here is eight bits in a row, and above each one its weight: 128, 64, 32, 16, 8, 4, 2, 1. To read the number, add the weights where there is a 1.
- In this example 128 plus 32 plus 16 plus 4 gives 180. The same eight bits can be written as 180 in decimal, or as B4 in hexadecimal - it is the same value, just a shorter way of writing it.
- Now the pattern to remember: with n bits you can make two to the power n different values. One bit gives 2, four bits give 16, eight bits give 256, and thirty-two bits give about 4.3 billion - which is why there are that many internet addresses in IPv4.
- And because memory is addressed with bits, sizes also come in powers of two: one kilobyte is 1024 bytes, not 1000.
== IF ASKED ==
If someone asks why 1024: k address bits give 2^k locations, so capacities naturally land on powers of two.

## Slide 4
02 · STORAGE ELEMENTS
A bit needs a circuit that can hold a state
Any stable two-state circuit is a bit cell. Three you should know:
A. SR LATCH
Two cross-coupled NOR gates. The feedback loop keeps the value alive while power is on.
NOR
NOR
R
S
Q
Q̅
B. D FLIP-FLOP
The standard 1-bit cell. Samples D only at a clock edge, so timing is predictable.
D FF
D
CLK
Q
Q̅
Q(next) = D on every rising clock edge
C. DRAM CELL
One transistor and one capacitor: charge = 1, no charge = 0.
bit line
word line
Cs
Needs refreshing every ~64 ms
THE TRADE-OFF
Flip-flop: ~6 transistors per bit, no refresh, fast — the right choice inside the CPU.
DRAM cell: 1 transistor + 1 capacitor, needs refresh — the right choice for gigabytes.
SAY THIS: A flip-flop remembers one bit by feeding its own output back into itself.
Binary Storage and Registers
04
Notes: == SAY THIS (one line) ==
A flip-flop remembers one bit by feeding its own output back into itself.
== FULL SCRIPT ==
- A bit has to survive after we stop sending it, so we need a circuit that can hold a state. There are three you should know.
- First, the SR latch: two NOR gates whose outputs feed each other's inputs. Because each gate keeps the other going, the value stays put with no clock at all. It is simple, but it reacts to its inputs at any time, which makes large designs messy.
- Second, the D flip-flop. It only looks at its input at the moment the clock ticks - the rising edge. So the whole circuit moves in step, and we get predictable timing. This is the standard one-bit memory, and it is what a register is built from.
- Third, the DRAM cell used in main memory: one transistor and one capacitor. Charge on the capacitor means 1, no charge means 0. It is tiny, so you get gigabytes, but the charge leaks away, so it must be refreshed about every 64 milliseconds.
- That is the trade-off to remember: a flip-flop uses about six transistors per bit and never needs refreshing - fast, and used inside the processor. A DRAM cell uses one transistor plus a capacitor and needs refresh - cheap and dense, and used for main memory.
== IF ASKED ==
If asked why DRAM needs refreshing: the capacitor leaks, so every cell is read and written back periodically.

## Slide 5
03 · THE REGISTER
A register is n flip-flops sharing one clock
It stores one binary word and is read or written as a unit — selected by name, not by address.
FF
bit 3
D₃
Q₃
FF
bit 2
D₂
Q₂
FF
bit 1
D₁
Q₁
FF
bit 0
D₀
Q₀
CLK
one 4-bit register — value stored = Q₃Q₂Q₁Q₀
•
One clock, one update. All bits change together, so a word is never half-written.
•
Width = flip-flop count. An 8-bit register is 8 flip-flops.
Registers you will meet inside a CPU
Reg | Full name | Holds
PC | Program Counter | address of the next instruction
IR | Instruction Register | the instruction being decoded
MAR | Memory Address Register | address sent to memory
MDR | Memory Data Register | data read / to be written
ACC | Accumulator | intermediate ALU result
SP | Stack Pointer | top of the stack
PSW | Status / Flags | zero, carry, sign, overflow
Register transfer notation
R2 ← R1 copy R3 ← R1 + R2 add
Read right to left: the source is copied, the destination overwritten.
SAY THIS: A register is a row of flip-flops that all take a new value at the same instant.
Binary Storage and Registers
05
Notes: == SAY THIS (one line) ==
A register is a row of flip-flops that all take a new value at the same instant.
== FULL SCRIPT ==
- A register is nothing new. It is a group of flip-flops, one per bit, sharing one clock line.
- Because all of them hear the same clock edge, all bits change together. You never read a register and find half the new value and half the old one.
- The width is just the count: an eight-bit register is eight flip-flops, a sixty-four-bit register is sixty-four. And a register has no address - the instruction names it directly, which is why using it costs one cycle instead of a trip to memory.
- The table shows the registers you meet inside a processor. The program counter holds the address of the next instruction, which is what makes a program a sequence. The instruction register holds the instruction being decoded. The memory address and memory data registers are the only way to talk to memory. The accumulator keeps an intermediate result, the stack pointer makes function calls possible, and the status register holds the flags used by conditional branches.
- Finally, the notation. R2 arrow R1 means copy R1 into R2. Read it right to left: the source is copied, the destination is overwritten. It only happens when the control signal for that transfer is 1.
== IF ASKED ==
If asked 'does R1 lose its value?' - no, a transfer is a copy.

## Slide 6
04 · CONTROL
Control: load, shift, and the shared bus
A register only does something when a control signal says so — and only one output may drive the bus at a time.
(a) Parallel load
A 2:1 mux in front of each flip-flop decides: new data, or hold.
D0
0/1
FF
Q0
D1
0/1
FF
Q1
D2
0/1
FF
Q2
D3
0/1
FF
Q3
LOAD
Load = 1 → mux passes D, register takes the word. Load = 0 → mux feeds Q back, value is held.
(b) Shift and rotate
FF3
FF2
FF1
FF0
serial in
out
Wire each Q to the next D and every bit moves one place per clock: left shift ×2, right shift ÷2, rotate keeps every bit.
Clock | Bits (init 1011)
start | 1011
1 | 0101 (out 1)
2 | 0010 (out 1)
(c) One bus, one driver
Tri-state buffers have a third output state, high-Z, so many registers can share one bus — but only one enable may be active.
Two registers enabled at once → contention, a short circuit, not just a wrong value.
SAY THIS: A register changes only when a control signal tells it to - and only one register may drive the shared wire.
Binary Storage and Registers
06
Notes: == SAY THIS (one line) ==
A register changes only when a control signal tells it to - and only one register may drive the shared wire.
== FULL SCRIPT ==
- Three small ideas control everything.
- One: parallel load. In front of every flip-flop there is a two-to-one selector. If the Load signal is 1, the selector passes the new data in. If Load is 0, it feeds the flip-flop's own output back, so the value is held. That is why processors have write-enable signals.
- Two: shifting. Connect each flip-flop's output to the next one's input, and with each clock every bit moves one place. Shifting left multiplies by two, shifting right divides by two, and a rotate sends the bit that falls off one end back in at the other end so nothing is lost. The little table shows 1011 moving right, one position per clock.
- Three: the bus. If every register had its own private path to every other register, the wiring would grow with the square of the number of registers. Instead they all share one bus, through tri-state buffers which can be 0, 1, or disconnected - that third state is called high impedance.
- But here is the rule: exactly one register may be enabled at a time. If two drive the wire together, one tries to pull it high while the other pulls it low, and that is a short circuit, not just a wrong value.
== IF ASKED ==
If asked what the third state is: high impedance, electrically disconnected, so the wire is left alone.

## Slide 7
05 · PLACEMENT AND EXAMPLE
Where registers sit, and one worked example
Registers are the fastest, smallest storage in the machine — here is why, and what that buys us.
Registers
16–32 per core · < 1 ns · flip-flop
Cache L1/L2/L3
KB–MB · 1–10 ns · SRAM
Main memory
GB · 50–100 ns · DRAM + refresh
SSD / HDD
TB · µs–ms · blocks
← faster + costlier larger + cheaper →
WHY NOT ALL REGISTERS?
A flip-flop is ~6 transistors per bit; a DRAM cell is 1 + 1 capacitor, so registers would be ~6× the area.
One 8-bit register, R1 = 0000 1101 (13)
LOAD 11010110
1
1
0
1
0
1
1
0
= 214
SHL 1
0
0
0
1
1
0
1
0
= 26
SHR 1
0
0
0
0
0
1
1
0
= 6
ROL 1
1
0
0
0
0
1
1
0
= 134
What each operation did
Load overwrites all eight bits at once.
Shift moves every bit one place: left ×2, right ÷2.
Rotate returns the escaping bit, so no 1 is ever lost.
SAY THIS: Registers are the fastest and smallest storage, because they are built from flip-flops.
Binary Storage and Registers
07
Notes: == SAY THIS (one line) ==
Registers are the fastest and smallest storage, because they are built from flip-flops.
== FULL SCRIPT ==
- The bit in a register and the bit in main memory are logically the same, but physically very different.
- Registers sit inside the processor: a few dozen of them, read in under a nanosecond. Cache is next, kilobytes to megabytes at a few nanoseconds. Main memory is gigabytes but takes tens of nanoseconds, and a disk takes microseconds to milliseconds.
- Why not make everything registers? Because a flip-flop costs about six transistors per bit while a DRAM cell costs one transistor and a capacitor. You could never fit gigabytes that way.
- Now one worked example, all on the same eight flip-flops. R1 holds 0000 1101, which is 13.
- A load with 11010110 overwrites the whole word at once - that is the load enable doing its job. A left shift gives 0001 1010, which is 26: doubled. A right shift gives 0000 0110, which is 6: the half that did not fit is lost. A rotate gives 1000 0110, which is 134, and nothing was lost because the bit that left one end came back at the other.
- Same hardware every time. Only the control signals changed.
== IF ASKED ==
If asked why 13/2 is 6 and not 6.5: shifting drops the remainder - it is integer division.

## Slide 8
Summary and questions
Five sentences that carry the topic.
SAY THIS: binary, the bit cell, the register, the switches.
01
Binary is a hardware decision.
Two stable states are cheap, fast and noise-tolerant; n bits give 2ⁿ patterns.
02
A bit is held by a bistable circuit.
Flip-flops for speed in the CPU, capacitors for density in DRAM.
03
A register is n flip-flops on one clock.
All bits update together, so a word is never read half-written.
04
Control signals decide what happens.
Load to write, shift to move, tri-state enables to share one bus.
05
Registers top the hierarchy.
Fast and small because they are flip-flops; memory is big and slow by design.
LIKELY QUESTIONS
Why 2ⁿ and not n²?
Each extra bit doubles the patterns.
Register vs. cache?
Register: by name, ~1 cycle. Cache: by address.
Why refresh DRAM?
The capacitor charge leaks away.
Why only one bus driver?
Two enabled outputs short the line.
SOURCES
Mano, Computer System Architecture, 3rd ed. — Ch. 2, 4.
Stallings, Computer Organization and Architecture, 10th ed. — Ch. 3, 4.
Patterson & Hennessy, Computer Organization and Design — Ch. 4.
Thank you — questions are welcome.
Notes: == SAY THIS (one line) ==
Five sentences: binary, the bit cell, the register, the control signals, and the hierarchy.
== FULL SCRIPT ==
- To finish, five sentences.
- One: binary is a hardware decision. Two states are cheap and reliable, and n bits give two to the power n values.
- Two: a bit is held by a circuit that can sit stably in one of two states - a flip-flop for speed, a capacitor for density.
- Three: a register is a row of those flip-flops on one clock, so a word is never read half-written.
- Four: control signals decide what happens - load to write, shift to move, tri-state enables to share one bus, one driver at a time.
- Five: that is exactly why the hierarchy looks the way it does - fast and tiny at the top, slow and huge at the bottom.
- On the right are the four questions I would expect, with short answers. Thank you - I am happy to take questions.
== IF ASKED ==
No expected question on this slide.