## Slide 1
1
0
1
1
0
0
1
0
1
1
0
1
COMPUTER ORGANIZATION AND ARCHITECTURE
Binary Storage
and Registers
How a computer holds a 1, a 0, and a whole number inside the CPU.
Presented by <Your Name>
Roll no. / Section <Roll No>
Theory Presentation · 15 minutes
Notes: Good morning. My topic is Binary Storage and Registers.
Two questions drive this whole presentation: first, how does a machine that only
understands ON and OFF actually keep a value? Second, where does it keep the value
while it is working on it? The answer to the first is the binary storage cell, and
the answer to the second is the register. Everything else in the CPU - the ALU, the
control unit, the buses - is built on top of these two ideas.

## Slide 2
AGENDA
What we will cover
01
Representing data in binary
bits, bases, and how many values fit in n bits
02
Binary storage elements
flip-flops, latches, and the DRAM capacitor cell
03
What a register really is
n flip-flops side by side with a common clock
04
Register transfer and control
R1 ← R2 notation, load enable, tri-state bus
05
Register file and memory hierarchy
where registers sit, and why they are fastest
06
Worked example and summary
one 8-bit register, shifted, rotated and loaded
Binary Storage and Registers
02
Notes: Here is the route. We start from how values are written in binary, then look at the
physical element that stores one bit, then scale that up to n bits to get a register.
After that we look at how registers talk to each other - register transfer notation,
the load signal, and the shared tri-state bus. Finally we place registers in the
memory hierarchy and finish with a small worked example.

## Slide 3
01 · REPRESENTATION
Why binary? What can one bit hold?
Digital hardware is cheapest and most reliable when it only has to distinguish two states.
Two stable states
A transistor is reliably fully OFF or fully ON. Adding a third or fourth level means reading a tiny voltage difference — noise eats it.
Noise immunity
A 0 or 1 is a range, not an exact voltage. Anything below ~0.8 V reads 0, anything above ~2.0 V reads 1, so small disturbances are harmless.
Boolean algebra
Two-valued logic has a complete, simple algebra (AND, OR, NOT), so circuits can be designed and minimised mathematically.
One bit, two values
0
LOW / OFF / FALSE
1
HIGH / ON / TRUE
Two states -> one bit can answer exactly one yes/no question.
So how much can n bits hold?
Bits (n) | Distinct patterns | Unsigned range | Typical use
1 | 2 | 0 – 1 | flag
4 | 16 | 0 – 15 | one hex digit
8 | 256 | 0 – 255 | byte / ASCII char
16 | 65,536 | 0 – 65,535 | half-word
32 | 4.29 × 10⁹ | 0 – 2³²−1 | word / IPv4
64 | 1.84 × 10¹⁹ | 0 – 2⁶⁴−1 | long / address
In general: n bits → 2ⁿ distinct patterns.
Binary Storage and Registers
03
Notes: Why binary at all? Because a transistor that only has to be fully off or fully on is
cheap, fast and immune to small noise. If we tried to store four voltage levels in
one cell, a little noise would corrupt the value.
A single bit gives us exactly two values. With n bits we get two to the power n
patterns. Eight bits is 256 - enough for a character in ASCII. Thirty-two bits gives
about 4.3 billion patterns, which is why IPv4 ran out of addresses. This table is
worth remembering; it explains why word sizes are 8, 16, 32 and 64.

## Slide 4
01 · REPRESENTATION
Writing the same value in different bases
Binary is what the hardware stores; octal and hex are just compact ways for humans to write it.
One byte = 8 bits = 2 hex digits
1
0
1
1
0
1
0
0
b7
b6
b5
b4
b3
b2
b1
b0
MSB ← position weights → LSB
Base | Name | Digits used | Same value
2 | Binary | 0, 1 | 10110100₂
8 | Octal | 0 – 7 | 264₈
10 | Decimal | 0 – 9 | 180
16 | Hexadecimal | 0 – 9, A – F | B4₁₆
Why hex is everywhere
•
4 bits = 1 hex digit. Grouping is mechanical — no mental arithmetic.
•
Shorter to read. 0xB4 beats 10110100 in a memory dump.
•
Used for addresses, machine code, colour codes (#0E7C86).
CONVERT 10110100₂ BY HAND
weights: 128 + 32 + 16 + 4 = 180
hex: 1011 0100 → B 4 → 0xB4
NOTATION YOU MAY SEE IN TEXTBOOKS
1011 0100₂ = 0b1011_0100 = 0xB4
three ways to write the same byte
Binary Storage and Registers
04
Notes: The same eight bits can be written four ways. Binary is what the register physically
holds. Octal groups three bits, which is why old machines used it. Hexadecimal groups
four bits, so one byte is exactly two hex digits - that is the reason hex is used in
debuggers and memory dumps.
To convert by hand, add the weights of the 1 bits: 128 plus 32 plus 16 plus 4 gives
180. For hex, split the byte into two nibbles: 1011 is B, 0100 is 4, so 0xB4.

## Slide 5
01 · REPRESENTATION
From a bit to a terabyte
Storage is counted in powers of two, because addressing is binary.
1 bit
a single 0 or 1
smallest unit
1 nibble
4 bits
1 hex digit
1 byte
8 bits
1 character
1 word
16 / 32 / 64 bits
one CPU operation
Size | Value in bytes | Power of two
1 KB | 1,024 | 2¹⁰
1 MB | 1,048,576 | 2²⁰
1 GB | 1,073,741,824 | 2³⁰
1 TB | 1.0995 × 10¹² | 2⁴⁰
Why 1024 and not 1000?
An address of k bits can select exactly 2ᵏ locations, so memory sizes come out as powers of two. 1 KB = 2¹⁰ bytes.
Word length matters
It is the number of bits the CPU moves and processes at once. Wider word → more data per cycle, larger registers, but more hardware.
Binary Storage and Registers
05
Notes: Now the units. A nibble is four bits, a byte is eight, and a word is the natural
chunk the processor works on - 16, 32 or 64 bits depending on the architecture.
Note that 1 KB is 1024 bytes, not 1000. That is not an accident: with k address
bits you can select exactly 2 to the k locations, so capacities naturally land on
powers of two. Disk manufacturers use 1000, which is why a 500 GB drive shows as
about 465 GiB in your file manager.

## Slide 6
02 · STORAGE ELEMENTS
Where does one bit physically live?
Any circuit that can hold a state stably is a bit cell. Three common ones:
A. SR LATCH
Two cross-coupled NOR gates. The feedback loop keeps the value alive as long as power is on.
NOR
NOR
R
S
Q
Q̅
No clock: it simply stays put. Level-sensitive.
B. D FLIP-FLOP
The industry standard 1-bit cell. Captures D only at a clock edge, so timing is predictable.
D FF
D
CLK
Q
Q̅
Q(next) = D
Edge-triggered: changes only on CLK 0 → 1. This is what a register is built from.
C. DRAM CELL
One transistor and one capacitor hold the bit.
bit line
word line
Cs
Needs refreshing ~every 64 ms
The capacitor leaks, so the value must be read and rewritten. Dense and cheap, but volatile.
Key idea: storage = a circuit that can sit stably in one of two states; the flip-flop is the building block, the capacitor is the cheap alternative.
Binary Storage and Registers
06
Notes: This slide answers the physical question: what actually remembers a bit?
(a) The SR latch: two NOR gates feeding each other. Because each gate drives the
other, the loop keeps its state indefinitely - it is literally a circuit that argues
with itself into a stable answer. Cheap, but level-sensitive.
(b) The D flip-flop: the workhorse. It only samples D on the rising edge of the
clock, so the whole design has a predictable rhythm. When we say a register is n
flip-flops, this is the box we mean.
(c) The DRAM cell: one transistor and one capacitor. Charge means 1. It is tiny, so
you get gigabits per chip, but the charge leaks and must be refreshed every few tens
of milliseconds. That is the trade-off between registers and main memory.

## Slide 7
03 · THE REGISTER
A register is n flip-flops sharing one clock
Definition: a group of flip-flops that stores one binary word and is read or written as a unit.
FF
bit 3
D₃
Q₃
FF
bit 2
D₂
Q₂
FF
bit 1
D₁
Q₁
FF
bit 0
D₀
Q₀
CLK
all flip-flops sample together
one 4-bit register — value stored = Q₃Q₂Q₁Q₀
What this gives you
•
One clock, one update. All bits change simultaneously, so the word is never seen half-written.
•
Width = number of flip-flops. 8-bit register = 8 FFs, 64-bit = 64 FFs.
•
No address needed. It is selected by name, not by a memory address, so access is a single cycle.
R1 : 4-bit register, R1 = 1011
Binary Storage and Registers
07
Notes: Now we scale a bit up. A register is just n flip-flops wired side by side, sharing
one clock line. Because they all sample the clock edge at the same instant, the word
is written atomically - you never read a register and find half of the new value and
half of the old.
The width is not magic: an 8-bit register is eight flip-flops, a 64-bit register is
sixty-four. And crucially, a register has no address. You select it by name in the
instruction, which is why it takes a single cycle rather than a memory round trip.

## Slide 8
03 · THE REGISTER
Register transfer notation: R1 ← R2
The notation that describes what happens between registers, independent of the hardware that does it.
SYNTAX
R2 ← R1 transfer (copy)
R3 ← R1 + R2 add
R4 ← R3 − 1 decrement
R1 ← 0 clear
Read it right to left: the source is read and copied, the destination is overwritten. The source keeps its value — a transfer is a copy, never a move.
Every transfer happens under a control function
A statement only executes when its enable signal is 1. In hardware this becomes a set of gate signals, not a line of code.
if (T3 = 1) then R2 ← R1
The hardware behind one arrow
R1
source
R2
destination
tri-state
EN = T3
bus
LOAD
T3 : R2in
control signal
Gate R1 onto the bus (its output enable), then pulse R2's load line. Nothing moves unless both control signals are asserted on the same cycle.
R1out | R2in | What happens
0 | 0 | bus idle, R2 unchanged
1 | 0 | R1 drives bus, nobody loads
0 | 1 | R2 loads whatever is on the bus
1 | 1 | R2 ← R1 (the transfer)
Binary Storage and Registers
08
Notes: Register transfer notation is the language we use to describe data movement. R1 arrow
R2 means copy R1 into R2. Read it right to left: the destination is overwritten and
the source is untouched.
Notice the condition - if T3 is 1, then the transfer happens. Real hardware has no
"if"; the T3 line simply enables the gates.
On the right is the actual circuit: R1's output passes through a tri-state buffer
whose enable is R1out, so R1 drives the shared bus. R2's load enable R2in then
captures the bus on the next clock edge. Only when both are 1 does the transfer
complete - that is the last row of the table.

## Slide 9
03 · THE REGISTER
Registers you will meet inside a CPU
Small in number, but each one has a specific job in the fetch–decode–execute cycle.
Register | Full name | What it holds | Why it exists
PC | Program Counter | address of the next instruction | keeps the program moving
IR | Instruction Register | the instruction being decoded | decouple fetch from execute
MAR | Memory Address Register | address sent to memory | drives the address bus
MDR | Memory Data Register | data read / to be written | buffers the data bus
ACC | Accumulator | intermediate ALU result | classic 1-operand machines
SP | Stack Pointer | top of the stack | calls, returns, locals
PSW | Status / Flags | zero, carry, sign, overflow | conditional branches
GPR | General Purpose | operands and addresses | compiler's scratch space
Three that matter most
PC
Tells memory which instruction to fetch next.
IR
Holds what was fetched while it is decoded.
MAR / MDR
The only route to memory: address out, data in.
Typical count: 16–32 registers per core, versus billions of memory cells.
Register file: all the general-purpose registers together, with two read ports and one write port, selected by register number inside the instruction.
All of these are the same hardware: n flip-flops with a load enable. Only the wiring around them differs.
Binary Storage and Registers
09
Notes: You do not build a CPU out of general logic alone - you give it a handful of named
registers, each with a job.
The PC holds the address of the next instruction; that is what makes a program a
sequence. The IR holds the instruction currently being decoded, which lets the fetch
unit run ahead of the execute unit. MAR and MDR are the interface to memory: MAR
drives the address bus, MDR buffers the data bus. The accumulator is the classic
one-operand design. The stack pointer makes function calls possible. The status
register makes conditional branches possible.
The important point at the bottom: all of these are the same circuit - n flip-flops
with a load enable. What differs is who is allowed to read and write them.

## Slide 10
04 · CONTROL
Controlling a register: the load enable
A register must know when to accept new data. One extra input, Load, solves it.
D inputs
2:1 MUX
flip-flop
D0
0/1
FF
Q0
D1
0/1
FF
Q1
D2
0/1
FF
Q2
D3
0/1
FF
Q3
hold path
LOAD
Load = 1: the MUX passes the D inputs → register takes the new word. Load = 0: the MUX feeds Q back into the flip-flop → value is held.
LOAD | CLK | Next state of register
0 | rising | unchanged (hold)
1 | rising | D₃D₂D₁D₀ (load)
x | no edge | unchanged
SYNCHRONOUS, NOT MAGIC
Changing D alone does nothing. The value is captured only on a clock edge while Load is high.
Binary Storage and Registers
10
Notes: A register with no control input is useless - it would overwrite itself on every
clock. So we add one signal, Load.
The trick is a two-to-one multiplexer in front of each flip-flop. When Load is 1 the
mux passes the external D input, so new data is captured. When Load is 0 the mux
feeds the flip-flop's own output back into its input - the register reloads its
current value, which means it holds.
Two consequences worth stressing. First, changing the data inputs alone does not
change the register; only the clock edge matters. Second, this is why write-enable
signals exist in every real processor.

## Slide 11
04 · CONTROL
Shift registers: moving bits, not copying them
Connect each flip-flop's output to the next one's input and bits travel one position per clock.
FF3
FF2
FF1
FF0
serial in
serial out
CLK
One clock per position — initial value 1011
Clock | FF3 | FF2 | FF1 | FF0 | out
start | 1 | 0 | 1 | 1 | –
1 | 0 | 1 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 0 | 1 | 0
Each column keeps its value for one clock, then passes it on.
Four ways to wire the ends
SISO
Serial in, serial out
one bit at a time; delay line
SIPO
Serial in, parallel out
serial link → byte
PISO
Parallel in, serial out
byte → serial link
PIPO
Parallel in/out
plain buffer register
SHIFT = × 2 OR ÷ 2
Left shift doubles; right shift halves (the bit shifted out is lost).
Binary Storage and Registers
11
Notes: A shift register is the same flip-flops, but each Q output is wired to the next
flip-flop's D input instead of to the outside world. One clock moves every bit one
position.
Follow the table: we start with 1011, which is 11. After one clock, FF3 receives a
0 from the serial input and the old value moves right, giving 0101 - the 1 that fell
off the end appears at the output. That is eleven divided by two.
The four configurations are just choices about which ends are parallel and which are
serial: SISO for a delay line, SIPO to receive a serial line into a byte, PISO to
transmit. And the shift itself is a cheap multiply or divide by two, which is why
compilers love powers of two.

## Slide 12
04 · CONTROL
Many registers, one bus: tri-state buffers
Connecting every register to every other register needs n² wires. A shared bus needs n.
A tri-state buffer has three output states: 0, 1, and high-impedance (Z). High-Z means electrically disconnected, so many outputs can share one wire — provided only one of them is enabled at a time.
R1
R1out
R2
R2out
R3
R3out
common bus (one word wide)
R4
destination
The one rule that must never break
Exactly one output enabled at a time. Two drivers on one wire = bus contention: a short circuit, not just a wrong value.
R1out | R2out | R3out | Bus state
1 | 0 | 0 | carries R1 ✓
0 | 1 | 0 | carries R2 ✓
0 | 0 | 0 | floating (Z)
1 | 1 | 0 | contention ✗
Cost of a bus: one transfer per cycle, but only one word wide — so wide buses and multiple buses are how CPUs get more done per clock.
Binary Storage and Registers
12
Notes: If every register had a dedicated path to every other register, the wire count grows
as n squared. Instead, all registers share a single common bus.
The enabling element is the tri-state buffer. Besides outputting 0 and 1 it has a
third state, high impedance - it looks like an open circuit. So several outputs can
sit on one wire, as long as only one is enabled.
The truth table on the right shows why exactly one enable must be high. Two drivers
at once is bus contention: one gate tries to pull the line to 5 volts while another
pulls it to 0, and the current can damage the chip.

## Slide 13
05 · PLACEMENT
Where registers sit: the memory hierarchy
Same bit, very different cost. Registers trade capacity for speed.
Registers
16–32 per core · < 1 ns · flip-flop
Cache (L1/L2/L3)
KB–MB · 1–10 ns · SRAM
Main memory (RAM)
GB · 50–100 ns · DRAM + refresh
SSD / HDD
TB · µs–ms · block device
← faster, smaller, costlier per bit slower, larger, cheaper →
Register vs. main memory
 | Register | RAM cell
Element | flip-flop | cap. + FET
Select | by name | by address
Access | < 1 cycle | many cycles
Capacity | bytes | gigabytes
Volatile | yes | yes (refresh)
Why not make all memory flip-flops?
A flip-flop is ~6 transistors per bit; a DRAM cell is 1 transistor + 1 capacitor. Same bit, ~6× the area and far more heat.
Registers exist because the CPU cannot wait 100 ns for every operand.
Binary Storage and Registers
13
Notes: Now the placement question. The bit stored in a register and the bit stored in RAM
are logically identical, but physically very different.
A register is built from flip-flops sitting inside the CPU; it is selected by name
and read in a fraction of a cycle. Cache is SRAM, a few nanoseconds. Main memory is
DRAM, tens of nanoseconds. Disk is microseconds to milliseconds.
Why not make everything registers? Because a flip-flop costs about six transistors
per bit while a DRAM cell costs one transistor and one capacitor. You could not fit
gigabytes on a chip that way, and the wiring would dominate.

## Slide 14
06 · EXAMPLE
Worked example: one 8-bit register
R1 = 0000 1101 (decimal 13). What do the control signals make it do?
LOAD R1 ← 11010110
Load = 1: the whole word is captured on the clock edge.
1
1
0
1
0
1
1
0
= 214
decimal
SHL R1, 1
Left shift: bits move left, 0 enters at LSB → ×2.
0
0
0
1
1
0
1
0
= 26
decimal
SHR R1, 1
Right shift: bits move right, MSB filled with 0 → ÷2.
0
0
0
0
0
1
1
0
= 6
decimal
ROL R1, 1
Rotate: the bit leaving MSB re-enters at LSB — nothing lost.
1
0
0
0
0
1
1
0
= 134
decimal
READING THE RESULT
13 in binary: 13 = 8 + 4 + 1, so bits 3, 2 and 0 are set → 0000 1101.
Shift left doubles: 0000 1101 → 0001 1010 = 26. Every bit weight doubled.
Shift right halves: the 1 shifted out past bit 0 is lost, so 13 / 2 = 6, not 6.5.
Rotate preserves bits: the 1 leaving the left end returns on the right, so the number of 1s never changes.
Same hardware, different control signals.
Binary Storage and Registers
14
Notes: Let us put the pieces together on one register holding 0000 1101, which is 13.
A load with 11010110 overwrites the whole word - that is what the parallel load
enable buys us.
A left shift gives 0001 1010, which is 26 - exactly double. A right shift gives
0000 0110, which is 6; the half that did not fit is lost, so this is truncating
division.
A rotate is different: the bit pushed off the left end comes back in on the right,
giving 10000110 = 134. Nothing is lost.
The point of this slide is that all four operations used the same eight flip-flops.
Only the control signals and the wiring around them changed.

## Slide 15
RECAP
Summary
Five sentences that carry the whole topic.
01
Binary is a hardware decision.
Two stable states are cheap, fast and noise-tolerant; n bits give 2ⁿ patterns.
02
A bit is held by a bistable circuit.
Flip-flops for speed inside the CPU, capacitors for density in DRAM.
03
A register is n flip-flops with one clock.
All bits update together, so a word is never read half-written.
04
Control signals decide what happens.
Load enable to write, tri-state enables to drive a shared bus, one driver at a time.
05
Registers are the top of the hierarchy.
Fast and tiny because they are built from flip-flops; memory is big and slow because it is built from capacitors.
Binary Storage and Registers
15
Notes: To consolidate. One: binary is not a convention, it is a hardware decision - two
states are reliable, and n bits give two to the n patterns.
Two: a bit survives because of a bistable circuit, a flip-flop or a capacitor.
Three: a register is that circuit repeated n times with a common clock, so updates
are atomic.
Four: what the register does is decided by control signals - load to write, tri-state
enables to talk on the bus.
Five: and that is exactly why the hierarchy looks the way it does - flip-flops are
fast and small in number, capacitors are slow and enormous in number.

## Slide 16
Thank you
Questions are welcome.
SOURCES
•
M. Morris Mano, Computer System Architecture, 3rd ed. — Ch. 2 (registers, register transfer) and Ch. 4 (micro-operations).
•
William Stallings, Computer Organization and Architecture, 10th ed. — Ch. 3 (top-level structure), Ch. 4 (cache).
•
Patterson & Hennessy, Computer Organization and Design — Ch. 4 processor datapath and registers.
•
NPTEL / IIT lectures on digital logic: flip-flops, registers, tri-state buses.
LIKELY QUESTIONS
Why 2ⁿ and not n²?
Each bit doubles the patterns.
Register vs. cache?
Register = by name, 1 cycle; cache = by address.
Why refresh DRAM?
Capacitor charge leaks away.
Why only one bus driver?
Two drivers short the wire.
Notes: Thank you. Before questions, these are the four follow-ups I would expect, and short
answers to each.
Why two to the n? Because each additional bit doubles the number of distinct
patterns.
Register versus cache? A register is selected by name in the instruction and takes
about one cycle; cache is selected by address and takes a few cycles.
Why does DRAM need refresh? The capacitor leaks, so every cell must be read and
rewritten periodically.
And why only one bus driver? Because two enabled outputs would fight each other and
short the line.